## Slide 1: A Systems Engineering Perspective of DTR
Focusing on Systems Architecture

## Slide 2: What is systems engineering?
“Systems Engineering is a transdisciplinary and integrative approach to enable the successful realization, use, and retirement of engineered systems, using systems principles and concepts, and scientific, technological, and management methods.”
-INCOSE Definition
https://www.incose.org/about-systems-engineering/system-and-se-definition/systems-engineering-definition
What is an engineered system?
A system designed or adapted to interact with an anticipated operational environment to achieve one or more intended purposes while complying with applicable constraints
Notes: System Engineering is responsible :
establishing, balancing and integrating stakeholders’ goals, purpose and success criteria, and defining actual or anticipated customer needs, operational concept and required functionality
establishing an appropriate process approach and governance structures, considering the levels of complexity, uncertainty, change, and variety;
generating and evaluating alternative solution concepts and architectures;
baselining and modelling requirements and selected solution architecture for each phase of the endeavor;
performing design synthesis and system verification and validation;
Considers both the problem and solution domains, to identify the role that the parts and the relationships between the parts play with respect to the overall behaviour and performance of the system
Determines how to balance all of these factors to achieve a satisfactory outcome.

## Slide 3: What does this mean?
Systems Engineering is
  A process to design the most suitable system
  To meet your intended purpose (need)
  For the required environment
  Given all of your constraints
  Other aspects of SE we don’t care as much about
Ultimately, the DTR “problem” is a Systems Engineering “problem”

## Slide 4: Why Systems Engineering?
We only have so much time
We only have so much money
We have a limited number of team members
We have to use our resources wisely
“Better is the enemy of good enough”

## Slide 5: What is our purpose*?
Defeat other teams in a one-on-one game of autonomous blimp soccer
How do we defeat them?
  Score goals
  Keep them from scoring goals
Win the Game
Score Goal
Deny Goal
*Purpose = problem, requirement, need (can be called many things)

## Slide 6: What is the required environment?
Indoors
Large open highbay
  Variable heights
  Rafters in ceiling
  Multiple catch points
  High volume air flow
LED lighting
Approx 180ft
Approx
67ft

## Slide 7: Environment (cont’d)
Goals
  Square
  Triangle
  Circle
  Orange and Yellow Retroflective
    Color of interest dependent on home side
  Fixed locations
Game ball
  22” Round
  Green/Yellow mylar
  Randomly placed
Other teams’ vehicles

## Slide 8: What are our constraints
For every 5:00 period must use Autonomy for 4:30
  Can use manual control for :30
Schedule
  time to acquire parts,
  time to perform engineering (design, integration, testing)
  Competition starts 4/18
Cost - $2-5K total budget
Size-Weight-Power (SWaP)
  Size – no more than 50ft3 of He
  Weight
    Lift capacity of He is 0.06-0.07lb/ft3
    ~3lb total lift for 50ft3 (including balloon)
    Negative buoyancy cannot exceed 100g
  Power
    LiPo – best power/weight ratio
    Limited by weight
    Enough power to last 30min game time (or method to swap batteries)
Others? –imposed or derived from required environment?
  Strong air currents
  Proximity to other blimps/obstacles

## Slide 9: System Architecture
3 Layers of Architecture:
Functional – what functions will the system need to perform
Logical – grouping of functions into logical components
Physical – HW/SW components that realize logical components that perform functions

## Slide 10: SE – Functional Design
Win the Game
Score Goal
Deny Goal
Manipulate Game Ball
Find Goal
Find Game Ball
Maneuver System
???

## Slide 11: Flow Diagram – Scoring Goals
Manipulate Game Ball
Find Goal
Find Game Ball
Maneuver System
Perform Ball Search Pattern
Look for Ball
Ball Found
Maneuver to Ball
Capture Ball
Look for Goal
Goal Found
Maneuver to Goal
Perform Goal Search Pattern
Subject to Constraints

## Slide 12: Maneuver Functional to Logical
Maneuver System
Perform Ball Search Pattern
Maneuver to Ball
Perform Goal Search Pattern
Maneuver to Goal
Flight Controller
Joystick
Motors
Follow Flight Pattern
Detect Position of Ball
Sensors
Maintain course to ball
Follow Flight Pattern
Detect Position of Goal
Maintain course to goal
Subject to Constraints
*manual control

## Slide 13: Logical Decomposition
Flight Controller
Joystick
Motors
Sensors
Joystick Controller
Motor Controller
Sensor Interface
Energy
Physical mounting
Energy
Physical mounting
Energy
Physical mounting
Air Frame
Battery

## Slide 14: Flight Controller Logical to Physical Design
Flight Controller
Pix Racer
Single Board Computer (Rpi)
Other
Rpi Zero W 2
Rpi 4
Pros:
Already Procured
Flight Controller SW Built in
Integrated motor controller
Joystick interface
Integrated IMU
Low-Mid SWaP
Cons:
Steep learning curve (time)
No camera interface
Limited sensor interfaces
May require separate telemetry interface
Pros:
Low SWaP
Already Procured
Many functions alredy written
Multiple sensor interfaces
BT for Joystick interface
SSH for telemetry/offloading
Cons:
May require separate motor controller
Limited computational capacity
New interfaces require custom SW
Pros:
Reuse functions alredy written for Rpi Zero
Multiple sensor interfaces
BT for Joystick interface
Computational capacity for ML/Depth mapping
Cons:
HIGH SWap
May require separate motor controller
New interfaces require custom SW
Pros:
?
Cons:
Not procured
Limited existing knowledge

## Slide 15: How do we down select between options?
Test multiple configurations?
  What are the criteria? Comparison against constraints?
  What is the decision process?
Design with multiple configurations?
  How do we divide efforts?
  What is the decision process

## Slide 16: Verification that Physical Design performs necessary functions
Single Board Computer (Rpi)
Flight Controller
Follow Flight Pattern
Maintain course to ball
Follow Flight Pattern
Maintain course to goal
Sensor Interface
Joystick Controller
Can also fulfill other logical roles

## Slide 17: Repeat Process for all Functions
Find game ball
Manipulate game ball
Find goal

## Slide 18: Division of labor
Individual design teams
Group design
Build/Integrate/Test Cycles

## Slide 19: Maneuver Decompose into details
Maneuver System
Manual Control
Autonomous Control
Control Input
Open Loop Control
Closed Loop Control
Sensor Feedback
Joystick
Sensors
Motors
Joystick Interface
Motor
Controller
Physical Mounting
Sensor Interface
Physical Mounting
SWaP
Time
Cost
Flight Controller